## Slide 1: Homework 7 (Discussion)
Using the data “cr2247001_000000.LTA”, output the current velocities from the 90th ensemble to the 120th ensemble, after removing the “bottom-track” ship velocities. Show the ship track and current velocities on a map.
Compare the current velocities to those after removing the “GPS” ship velocities.
For those MAC users, you could direct use the files “uv_gps_90_120.txt” and “uv_bt_90_120” given in the class-file server (http://gofile.me/3P3ad/K8rdSnYve).

## Slide 2
兩邊經緯度的範圍不一樣且框框內的箭頭長度及方向不一樣

## Slide 3
Only difference I could see is at the bottom of the ship track (24.843°N 122.02°"E) the current velocities seems different.

## Slide 4
上圖流矢的分布相較下圖集中，而下圖流矢的分布相較上圖分散。比較兩圖最下方最突出的流矢(2017/06/29 02:05:08 , the 90th ensemble)，下圖的流速較快。以及兩圖的94th ensemble(2017/06/29 02:25:08)流矢也有不同的表現。

## Slide 5
洋流流速及流向皆略有不同。

## Slide 6
紅線為移除gps的速度；藍線則為移除bottom track的速度
可看出上半部的紅線幾乎和藍線重疊，但下半部兩顏色的線除方向不同，速度也不盡相同，藍線看起來也許是船體受到慣性影響，因此方向改變的較緩慢。

## Slide 7
平均流速
Remove Bottom-track : 239.4708 (mm/s)
Remove GPS : 235.9008 (mm/s)
流速減平均流速的誤差（平均）
Remove Bottom-track : 35.0188
Remove GPS : 49.4029

## Slide 9: ADCP Calibration
Bottom track and Navigation (GPS)

## Slide 10: Error sources of ADCP measurement
Noise of instruments
Sound absorption
Misalignment of the transducer relative to the ship’s keel
Interference by physical objects and ship‐induced turbulence
Ship motion

## Slide 11: Error sources of ADCP measurement
Noise of instruments
Sound absorption
Misalignment of the transducer relative to the ship’s keel
Interference by physical objects and ship‐induced turbulence
Ship motion

## Slide 12: Affecting the accuracy of ADCP
Misalignment Angle
Ship’s motion: Pitch and Roll
https://en.wikipedia.org/wiki/Aircraft_principal_axes
(Heading axis)

## Slide 13: Ocean-Current Homogeneity in a Horizontal Layer (REVIEW)
Error velocity: the difference between the two estimates of velocity
Non-homogeneous currents  large error vel.
Large errors of Pitch and Roll  large error vel.

## Slide 14: Velocity data (REVIEW)
Based on different kind of coordinates:
Beam coordinates: Velocity is parallel to each beam.
Earth coordinates: Velocity in north, east and up (We want this)
ADCP coordinates: Similar to earth coordinates but the velocity is relative to ADCP
Ship coordinates: Similar to ADCP coordinates except that heading is rotated into ship‘s forward and sideways.
Sources: ADCP Principles of Operation
(A Practical Primer), RDI, 2011

## Slide 15: Misalignment Angle
λ : mounting angle of ADCP to ship’s keel (船骨)
NE: earth coordinates
XY: ship coordinates
X’Y’: ADCP coordinates
γ: the angle of (X, Y) relative to (N, E) measured by the gyrocompass, because the the ship heading is not always along the ship track.
Osiński [Oceanologia, 2000]
Misalignment Angle
α = γ +λ
(positive for counterclockwise)
wind

## Slide 16: Velocity variables for different references

## Slide 17: Misalignment Angle
λ : mounting angle of ADCP to ship’s keel (船骨)
NE: earth coordinates (ug, vg)
XY: ship coordinates (ub, vb)
X’Y’: ADCP coordinates (ur,vr)
γ: the angle of (X, Y) relative to (N, E) measured by the gyrocompass, because the the ship heading is not always along the ship track.
Osiński [Oceanologia, 2000]
Misalignment Angle
α = γ +λ
(positive for counterclockwise)

## Slide 18: Velocity variables for different references
Then, what velocities we need to calibrate?
ship bottom-track velocities, ADCP relative velocities
Bottom-
track

## Slide 19: Coordinate Rotating (Fixing Misalignment Angle, α )

## Slide 20: Coordinate Scaling (uniform) (Fixing pitch & roll, β)
A value, 0.3o, of the beam orientation from the vertical results in a |β| of 1.01.
β

## Slide 21: Calculating α and β
Assume that are the ship velocities measured by the ADCP bottom track and are the ship velocities measured by the ship GPS. Then,
denotes the ensemble mean

## Slide 22: References
Joyce, T. M., 1989. On in Situ “Calibration” of Shipboard ADCPs. Journal of Atmospheric and Oceanic Technology, 6, 169-172.
Tang, T.-Y. and J.-C. Ma, 1995. A note on the accuracy of shipboard ADCP on Ocean Researcher I. Acta Oceanographica Taiwanica, 34, 71-81.
Osiński R.,2000. The misalignment angle in vessel-mounted ADCP. Oceanologia, 42 (3), 385-394.

## Slide 23: Start doing some practical exercises in class to calculate the α and β
Using the OR2_2247_20170628 data from the 90th ensemble to the 109th ensemble

## Slide 24: Getting ship velocities from WinADCP (5~10 mins)
Open “cr2247001_000000.LTA”
Output the ship velocities measured by the bottom track and GPS

## Slide 25: Looking at the ship velocity data

## Slide 26: Deleting the heading

## Slide 27: Read in data to PC (15 mins)
Use your tool to read in the and .
Again,
are the ship velocities measured by the ADCP bottom track and
are the ship velocities measured by the ship GPS.

## Slide 28: Calculating α and β (30 mins)
denotes the ensemble mean
from 90th ensemble to the 109th ensemble

## Slide 29: Calculating α and β (MATLAB codes)
d=load('ship_vel_gps_bt_ok');
ub=d(:,9);
vb=d(:,10);
ug=d(:,11);
vg=d(:,12);
tan_alpha=mean(ub.*vg-vb.*ug)/mean(ub.*ug+vb.*vg);
alpha=atand(tan_alpha)
beta=sqrt(mean(ug.^2+vg.^2)/mean(ub.^2+vb.^2))
## alpha=-0.77o, beta=1.0353.

## Slide 30: How to calibrate the current velocities using the α and β
Calculate the current velocities from the velocities relative to ADCP

## Slide 31: Velocity variables for different references

## Slide 32: Velocity variables for different references
Then, what velocities we need to calibrate?
ship bottom-track velocities, ADCP relative velocities
Bottom-
track

## Slide 33: Calculating the absolute water velocities after calibration
Removing bottom-track ship velocities:
Removing GPS ship velocities:

## Slide 34: Velocity variables for different references
{outputted}
{outputted}
Removing bottom-track ship velocities:

## Slide 35: Getting the relative water velocities from WinADCP (5~10 mins)

## Slide 36: Outputting the relative water velocities from WinADCP (5~10 mins)

## Slide 37: Looking at the data of relative water velocities

## Slide 38: Deleting the heading

## Slide 39: Calculating the absolute water velocities (bottom track)
Removing bottom-track ship velocities:

## Slide 40: Calculating the absolute water velocities (GPS)
Removing GPS ship velocities:

## Slide 41: Calculating the absolute water velocities (MATLAB codes)
d=load('uv_2247_no_ok.txt');
ur=d(:,9);
vr=d(:,10);
uw_bt=beta*((ur+ub)*cosd(alpha)-(vr+vb)*sind(alpha));
vw_bt=beta*((ur+ub)*sind(alpha)+(vr+vb)*cosd(alpha));
uw_gps=beta*(ur*cosd(alpha)-vr*sind(alpha))+ug;
vw_gps=beta*(ur*sind(alpha)+vr*cosd(alpha))+vg

## Slide 42: Plot results
Comparing the current velocities after removing bottom-tracked ship velocities and GPS ship velocities.